SO2 oxidation input data from Example 8-10, H. S. Fogler, "Elements of Chemical Reaction Engineering," 2nd ed., Prentice-Hall (1992):

The feed gas is 7900 lb-mol/h of 11% SO2, 10% O2, and 79% inert which is mostly N2. The simulation accounts for gas pressure drop down the adiabatic bed and the changing heat capacity of the gas as conversion changes.

-r_{SO2} = k sqrt{{P_{SO2}} over {P_{SO3}}} left [ P_{O2} - left ( {alignc P_{SO3}} over {K_{P} P_{SO2}} right )^2 right ]

k = "exp" left[ {-176008} over {alignc T} - 110.1 "ln"(T) + 912.8 right]

K_{P} = "exp" left[ {42311} over {alignc R T} - 11.24 right]

where k has units (lb-mol SO2/lb-catalyst/s/atm), KP has units (atm-1/2), and T has units (°R). This rate can be used above a conversion of SO2 of 5% and larger. Below that conversion, assume the rate is equal to the rate at 5% conversion.

%DELTA H_{R} (800 °"F") = -42471 "Btu/lb-mol-SO"_{2}

diameter of spherical catalyst pellets = 0.015 ft
bed void fraction = 0.45
bulk density of catalyst bed = 33.8 lb/ft3